## Slide 1: Memcached Prototype Architecture
Kimon Karras, Lisa Liu, Michaela Blot
March 2014

## Slide 2: Memcached Functionality Recap
Many popular websites share a similar basic architecture
Memcached is used by 85% of top 20 websites, 50% of top 5000 websites, up to 30% of servers in data centers
Users
Web Servers
Database
Users
Web Servers
Users
Web Servers
In-memory Cache Layer (x86)
In-memory cache relieves access load on main, disk-based SQL database, pushing scalability problem back to the web tier
Memcached clients
Memcached servers
Get value @key
Return value

## Slide 3: FPGA-based Dataflow Architecture
UDP/TCP
Offload Engines
Network
Interface
(10Gbps Ethernet)
DRAM
Standardized interface:
Key, value, meta-data
FPGA
Hash
Table
Value Store
Implemented in Vivado HLS
Request
Parser
Response Formatter
Hash
Table
Value Store
DRAM Controller
Memcached Pipeline
1. Receives network packets
3. Retrieve value address from hash table
4. Write/Read values into the memory
5. Compose the outgoing packet
6. Send packets to the network
Notes: Host code C: 565
Memcached RTL:
Binary Parser: 703
ASCII parser: 2741
Hash table: 3415
Value store: 2336
Binary Response: 396
ASCII Response: 2545
Others: 999+ 2357+459=3815
Total RTL: 16k

## Slide 4
Design Basics
Operating Frequency: 156 MHz
All I/O uses AXI4 Streams.
  I/O Buses are 184 bits wide.
  They adhere to the following format:
    0:63 – data
    64:66 – modulo (indicates the number of valid bytes in the data part)
    67 – EOP
    68 – SOP
    69:183 – network-related metadata
  Not all of the metadata bits are used.
Memory access uses 4 bus pairs.
  2 in the Hash Table (1 WR & 1 RD) & 2 in the Value Store (1WR & 1 RD)
  Each pair has a 512 bit wide data bus
  And a 24 bit command bus. The lower 10 bits make up the address & the following 8 the number of data words to be read to or written from.

## Slide 5
Design Resource Utilization
Memcached Pipeline Resource Use
  After HLS Synthesis:
  After Vivado Synthesis:

## Slide 6: Request Parser Architecture

## Slide 7: Request Parser Architecture
Request Parser
Binary Parser
ASCII Parser
Packet in
internal
unified format
Protocol Detection
Merge
Memcached requests
Protocol Detection recognizes if the incoming packet is binary or ASCII and routes it accordingly.
The corresponding parser completes the processing
The merge module then recombines them and sends them into the pipeline.

## Slide 8: Request Parser Module & Signal Names
RequestParser
binaryParser
asciiParser
Parser
Input
Selection
Parser
Output
Selection
inData
All signals one the block diagram are HLS streams.
The rp_packetSeqBuffer stream allows the ParserOutputSelection to maintain the same request order at the output side. It’s only 1 bit wide and identifies which parser processed a request.
outData
rp_packetSeqBuffer
rp_sel2ascii
rp_sel2bin
rp_bin2sel
rp_ascii2sel

## Slide 9: Binary Parser

## Slide 10: Binary Parser Architecture
inData
outData
bp_f
bp_r
FSM
FSM
Metadata
keyBuffer_rp
Metadata
valueBuffer_rp
metadataBuffer_rp
Consists of 2 FSMs, one reading data in & reformatting them and writing them to the output
It extracts and realigns key and value from the incoming request.
Other information (key length, value length, operation type, etc.) are stored in the metadata.

## Slide 11: ASCII Parser

## Slide 12: ASCII Parser Architecture
OpCode Extraction
Key Extraction
Flags Extraction
Expiraton
Extraction
Value Lengh
Extraction
Value
Extraction
Internal Pipeline Word
Packet
Input
Sideband channel
Key
Flags
Expiry
V Length
Value
Parser Output Formatter
Pipelined design
Each stage filters the data which it processes and passes on the rest.
All collected data is placed into queues.
The output logic fetches the data and outputs them in the memcached pipeline format.
Field Conversion
Field Conversion
Field Conversion
Juggler

## Slide 13: ASCII Parser Modules & Signals
ap_operation
ID
ap_flags
Extractor
ap_expiry
Extractor
ap_value
Length
Extractor
ap_valueStream
ap_outputLogic
ap_ascii2bin
Converter
ap_ascii2bin
Converter
ap_ascii2bin
Converter
ap_value
LengthJuggler
inData
ap_keyStreamGet
op2keySet
op2keyGet
keyBuffer
Get
keyLength
BufferGet
keyBuffer
Set
keyLength
BufferSet
value
Buffer
outData
Value
StartLoc
Value
vlExt2value
vlStart
Loc
ap_keyStreamSet
flagExt2
flagConv
flags
Buffer
expiry
Buffer
expExt2
expConv
vlExt2
vlJug
vlJug2
vlConv
valueLengthBuffer
Key2
flagsExt
Flags
StartLoc
flagsExt2ExpExt
Exp
StartLoc
expExt2
vlExt

## Slide 14: Hash Table Architecture

## Slide 15: Hash Table Architecture
Input
Logic
Hash Function
Concurrency Control Filter
Mem. Read
Compare
Mem.
Write
Output Logic
DRAM
Cmd.
DRAM
Data
DRAM
Cmd & Data
Original Packet Data
1. Stores Key, Value & metadata. Resizes Key. Creates HT metadata
2. Checks for race conditions between SET & GET operations due to memory latency
7. Injects value store address into the packet & forwards it.
4. Sends a read command to the memory.
3. Hashes the key to produce the hash table memory address to access.
5. Compares key length & key read from the hash table with the one in the request & decides if there is a match
6. Updates the hash table entry if SET/DEL. Forwards the value pointer in GET

## Slide 16: Hash Table Architecture
ht_input
Logic
bobJ
Concurrency
Control
mem
Read
ht_compare
memWrite
ht_outputLogic
memRdCtrl
memRdData
memWrData
Function is inlined into top
hashKey
Resizer
hash
hashMdBuffer
hashKeyBuffer
hashValueBuffer
ht_inData
ht_outData
in2cc
in2ccMd
hash2cc
dec2cc
cc2memRd
cc2memRdMd
memRd2compMd
memRd2comp
comp2memWrMd
memWrCtrl
memWr2out
comp2memWrKey
*
*
*
*
comp2memWrStatus
comp2memWrMemData
in2hash
in2hashKeyLength

## Slide 17: Value Store Architecture

## Slide 18: Value Store Architecture
Access Control
Dispatch
Demux
Remux
DRAM
Cmd.
DRAM
Data
Original Packet Data
Receive
Set
Path
DRAM
Data
DRAM
Cmd.
1. Checks for & avoids race conditions between gets and sets.
2. Stores Key & metadata. Forwards value address to the Dispatch for GETs. Sends value address & values to the Set Path for SETs.
3. Used by SETs only. Aggregates new value into 512 bit words & writes them to the value store.
4. Sends a read request to the Value Store.
5. Receives Data & converts them to 64-bit words.
6. Depending on the operation, recombines key, value & metadata accordingly & forwards it.

## Slide 19: Value Store Architecture
access Control
Dispatch
demux
remux
DRAM Cmd.
DRAM
Data
metadataBuffer
Receive
setPath
DRAM
Data
DRAM
Cmd.
getPath
Function is inlined into top
inData
outData
keyBuffer
accCtrl2demux
filterPopSet
filterPopGet
Demux2
setPath
Metadata
Demux2
getPath
getPath2remux
disp2rec
Demux2
setPath
Value

## Slide 20: Response Formatter Architecture

## Slide 21: Response Formatter Architecture
Response Formatter
Binary Resp.
ASCII Resp.
Packet in
internal
unified format
Protocol Detection
Merge
Works in the exact opposite way as the request parser
Also contains a protocol detection module & a merge module, which perform the exact same functionality as in the request parser.
Memcached Response

## Slide 22: Response Formatter Module & Signal Names
responseFormatter
binaryResponse
asciiResponse
response
Input
Selection
response
Output Selection
responseFormatterInData
rf_sel2bin
responseFormatteroutData
rf_sel2ascii
rf_bin2sel
rf_ascii2sel
rf_packeSeqBuffer
All signals one the block diagram are HLS streams.
The rp_packetSeqBuffer stream allows the ParserOutputSelection to maintain the same request order at the output side. It’s only 1 bit wide and identifies which parser processed a request.

## Slide 23: Binary Formatter

## Slide 24: Binary Response Formatter Architecture
inData
outData
bp_f
bp_r
FSM
FSM
Metadata
keyBuffer_rp
Metadata
valueBuffer_rp
metadataBuffer_rp
Consists of 2 FSMs, one reading data in & reformatting them and writing them to the output
Stores key, value & metadata coming from the bus into streams.
Output FSM then composes the appropriate response packet.

## Slide 25: ASCII Formatter

## Slide 26: ASCII Response Architecture
Internal Memcached Pipeline
Response Input
Key
Value
Metadata
Network
Output
Response Output
V Length Conversion
V Length Count
Merge_s2
Value Length
Op
Key Buffer
Value Buffer
opCode Buffer
Status Buffer
Merge_s1
Flags Conversion
Flags Count
V Length Juggler
Flags

## Slide 27: ASCII Response Architecture
Response Input
Response Output
Flags Conversion
V Length Conversion
Flags Count
V Length Count
Merge Stage 2
Stores key & value. Extracts relevant metadata field (flags, value length, op code).
opCode Buffer
Key Buffer
Value Buffer
V Length Juggler
Merge Stage 1
2. Convertes the flags field from binary to ASCII
2. Convertes the value length field from binary to ASCII
3. Counts the number of valid bytes in the ASCII value length field
5. Juggles the value length bytes to convert from big to little endian
6. Adds value length & delimiting characters into the result of the previous merge state
7. Combines all the various fields together to create the response packet.
Status Buffer
4. Merges flags & delimiting characters
3. Counts the number of valid bytes in the ASCII flags field

## Slide 28: ASCII Response Module & Signal Names
inputLogic
outputLogic
Ascii2bin
Flags
Ascii2bin
ValueLength
flagsCount
ValueLength
Count
merge_s2
opCodeBuffer
KeyBuffer
ValueBuffer
ValueLength
Juggler
merge_s1
statusBuffer
inData
outData
flgasExt2flagsConv
flagsConv2ol
vlExt2vlConv
vlConv2ol
mergedLength
mergedField
merge12merge2
merge12merge2Length
vlJugLength2merge
vlCountLength2vlJug
flagsCount2mergeS1
flagsLength2mergeS1
vlJug2merge
vlCount2vlJug

## Slide 29: Design Limitations
Only supports 4 basic commands:
  SET
  GET
  DELETE
  FLUSH
Does nor perform memory allocation. Hash value is truncated to derive the memory value.
Hash Table & Value Store are currently stored in BRAM.
Max. supported value size: 1024 Bytes
Max supported key size: 128 Bytes

## Slide 30: Vivado Project

## Slide 31: RTL Project Diagram
ETH
MAC
Network Extractor
Network Composer
Memcached
MIG
DRAM
Ethernet Converter In
Ethernet Converter Out
axis_outStream
Hash Table RD Adapter
Hash Table WR Adapter
Value Store RD Adapter
Value Store WR Adapter
All signals on this diagram are AXI4 Streams
memcachedPrototype
Receives & sends network data
2. Convert AXI4S Keep & Last signals to memcached SOP/EOP/modulo ones
3. Strips packet header away & stores network data (IP, MAC, etc.)
4. These 4 modules convert the memcached mem. access I/F to the AXI datamover one. Supports an ETH/IP/UDP header stack only
5. Recomposes the ETH/IP/UDP stack from the metadata received from the memcached pipeline.
4. Converts SOP/EOP/modulo signals back to AXI4S Keep & last ones.
HLS Blocks
IP Cores

## Slide 32: RTL Project Diagram
ETH
MAC
Network Extractor
Network Composer
Memcached
MIG
DRAM
Ethernet Converter In
Ethernet Converter Out
axis_i_0
axis_o_0
axis_inStream
axis_inExtractor
axis_outComposer
axis_outStream
Hash Table RD Adapter
Hash Table WR Adapter
Value Store RD Adapter
Value Store WR Adapter
All signals on this diagram are AXI4 Streams
memcachedPrototype

## Slide 33: Memcached Code Package (1)
Consists of:
  Vivado HLS 2013.4 Memcached Pipeline Project
  Vivado 2013.4 RTL project for the VC709 board
2-stage Verification :
  C Simulation
  RTL Simulation
Simulations consists of:
  3 patterns of SET & GET operations (SEQ1, SEQ2 & SEQ3)
  2 patterns testing failed SETs & GETs, as well as DELETEs & FLUSHes (ALLOPS, MANYSETS)
  Each pattern has 2 different input throughputs (1 & 12 Gbps) (Suffixes R01 & R12 respectively)
  Each pattern has an ASCII & a binary variant (Suffixes TXT & BIN respectively)
  RTL simulations also use 4 backpressure patterns per pattern (Suffixes BPRNO, BPR15-08, BPR20-07 & BPRRAND01).
In total there are:
  20 C simulations
  64 RTL simulations

## Slide 34: Memcached Code Package – Folder Structure
Memcached C++ Source Files
Location of exported IP core
Location of executable for C Simulation
Scripts, input & output files for C-based regression tests
RTL sources for RTL regression tests
Backpressure input files for RTL simulation
Packet input & output files for RTL simulation
RTL simulation results
Scripts for the RTL simulation
RTL simulation configuration files

## Slide 35: Creating a Vivado HLS project
There are two ways to run VHLS:
  Project mode
  Projectless mode
To use the former, open the GUI, create a project and add the source files.
To use the latter, run the run_hls.tcl script provided in the package.
This will create a project, add the files, compile them for C simulation, as well as synthesize and subsequently export the memcached pipeline as an IP core.
Using this option will cause the directory structure to deviate slightly from the one in the previous slide.

## Slide 36: Running C Simulations
Edit memcachedPipeline/sims/env.cSim to reflect the appropriate values for your system.
Launch memcachedPipeline/sims/memtest_deploy.py env.cSim
All test are run and a summary of the results is shown.
Output files end in the suffix –sim.result.txt
Report files of the compare between sim output and golden output have the suffix –sim.verification.txt
Hopefully you will get something like this:

## Slide 37: C Simulation Architecture
Mirrors that of the BRAM version of the real-life system.
Request
Parser
Response Formatter
Hash
Table
Value Store
Memcached Pipeline
BRAM Model Hash Table
BRAM Model Value Store
Memcached TB
Synthesizable Code
Non-synthesizable Code

## Slide 38: C Simulation Input File Format
Injects a number of idle cycles into the simulation (in this case 27)
Each line is read in per to function call (practically per clock cycle)
Network metadata (MAC, IP, port numbers, etc..)
Packet (memcached) data
SOP
Modulo
EOP
Valid
Output file looks identical (without the wait lines)

## Slide 39: Running RTL Simulations
Edit memcachedPipeline/rtlSim/regressionSims/sw/env.server to reflect the appropriate values for your system.
Launch memcachedPipeline/rtlSim/regressionSims/sw/memtest_deploy.py env.server
All test are run and a summary of the results is shown.
Output files end in the suffix –sim.result.txt
Report files of the compare between sim output and golden output have the suffix –sim.verification.txt
Results should look like this:

## Slide 40: RTL Simulation Output File Format
Injects a number of idle cycles into the simulation (in this case 27)
Each line is read in per to function call (practically per clock cycle)
Network metadata (MAC, IP, port numbers, etc..)
Packet (memcached) data
SOP, EOP & modulo are in this byte
1 is previous to last word, 7 is last word in a packet
Output file looks identical (without the wait lines)